## Slide 1: High Speed Rail in Japan - How to deliver utmost punctuality under heavy winter conditions -
Harutoshi HAYASAKA General Manager Technology Headquarters, Japan International Consultants for Transportation Co.,Ltd, JIC

## Slide 2: Main Contents
> Introduction of JIC
> Short History of Railway
> Shinkansen Network
> Main Features of the Shinkansen
> Annual Average Delay Time in Tokaido Shinkansen
> Framework for Implementation of Shinkansen Project
> Procedure of Shinkansen Construction
> Percentage of Structures on Shinkansen
> Measures against Snowfall
> Basic Points for Measures against Snow Damage
> Measures against Snow Damage and Weather Conditions
> Location of Snow-melting Facilities
> Specification of Sprinkler System
> Kinds of Equipment on Measures against Snowfall
> Flow Chart of Sprinkler Spray
> Conclusions

## Slide 3: Introduction of JIC

## Slide 4
Short History of Railway
1825 Commencement of Railway Operation in England
1856 Commencement of Railway Operation in Sweden
(Malmö - Göteborg)
1870 Start of Railway construction in Japan
1872 Commencement of Railway Operation in Japan
(Shimbashi – Yokohama) 29km
1964 Commencement of Shinkansen Operation
(Tokyo –Shin-Osaka)
1987 Privatization of Japanese National Railways
2013 Operation of 320km/h with Series E-5 at Tohoku Shinkansen

## Slide 5: Operational Range of Each JR Company

## Slide 6: Shinkansen Network
Tokyo
Sapporo
Shin-Osaka
Kagoshima-Chuo
2015
2016
Hokuriku Shinkansen
Joetsu Shinkansen
Tohoku Shinkansen
Hokkaido Shinkansen
Kyushu Shinkansen
Yamagata
Akita
[ Kagoshima Route ]
[ Nagasaki Route ]
Hakata
Sanyo Shinkansen
Tokaido Shinkansen
Constructed by JRTT
Under construction
Planning stage
(422km)
(533km)
In operation
(2,388km)
( )
Shin-Aomori
Shin-Hakodate
Nagano
Kanazawa
Niigata

## Slide 7: Shinkansen Vehicles

## Slide 8: Safety
Main Features of the Shinkansen
No passenger fatalities in 49 years
Reliability
High Density
Average delay time
less than 1 min
Up to 15trains per hour
Mass Transit
Approx. 890,000 passengers
Per day

## Slide 9: Annual Average Delay Time in Tokaido Shinkansen
Year
Annual Average Delay Time (minute/train)

## Slide 10: Framework for Implementation of Shinkansen Project
□ Separation of infrastructure and operation
JRTT (Government Agency)
（Infrastructure construction and ownership）
Lease of
facilities
JR (Private Companies)
（Shinkansen operation）
□ Financing
National (2/3) and local (1/3) governments bear financing
burden for the Shinkansen infrastructure. (Public works)
National Government
Local Governments
67 %
33 %
JRTT : Japan Railway Construction, Transport and Technology Agency

## Slide 11
Procedure of Shinkansen Construction
National government
Minister of Land, Infrastructure, Transport and Tourism
Decision of basic plan
Directs to conduct study
Submits study report
JRTT
Conducts study
based on the plan
Order
Operator (JR)
Environmental impact
assessment
Nomination of construction body
Nomination of operator
Construction body
(JRTT)
Nomination
Decision of provisional plan
Construction order
Draws up a
construction plan
Operator
(JR)
Approves the construction plan
Application
Approval
Consultation
Agreement
Start of
construction work
Completion
Operates
Lease

## Slide 12: Bridge
Structures on Shinkansen
Tunnel
Viaduct
Earth Structure

## Slide 13: Percentage of Structures on Shinkansen
0%
20%
40%
60%
80%
100%
Tokaido Shinkansen
Sanyo Shinkansen
Joetsu Shinkansen
Tohoku Shinkansen
Hokuriku Shinkansen
Tohoku Shinkansen
Kyushu Shinkansen
Tunnel
Bridge
Viaduct
Earth
Structure
(Tokyo-Shin Osaka)
(Takasaki-Nagano)
(Shin Osaka-Hakata)
(Tokyo-Morioka)
(Omiya-Niigata)
(Morioka-Hachinohe)
(Shin Yatsushiro-
Kagoshima Chuo)
OLD
NEW

## Slide 14: Measures against Snowfall
Snow disposal with vehicle
Sprinkling of water

## Slide 15: Basic Points for Measures against Snow Damage
>Equipment for aiming at scheduled train operation against the maximum 10-year snow depth and the maximum daily snowfall.
>Snow plough of the train removes the snow on the track during commercial operation.

## Slide 16: Measures against Snowfall and Weather Conditions

## Slide 17: Location of Snow-coping Facilities

## Slide 18
Cross-section of snow-storing type
Cross-section of sprinkler spray type
Semi snow shelter
Snow disposal with sloping eaves
of soundproof wall
Maintenance passage
Snow-storing line
R.L.+0.10m
Change the storing volume by
the thickness of roadbed RC
Standard snow-storing
Sprinkler
Maintenance passage
Measures against snowfall

## Slide 19: Snow-melting Formula
The formula consists of 5 heat quantities :
1 Quantity of Radiation Balance : Q R
2. Quantity of Conductive Heat at Slab: Q C
3. Expended Heat Quantity by Watering: Q H
4. Heat Quantity for Snow-melting : Q IS
5. Quantity of Turbulence Transmittable Heat : Q AE
Q H + Q R + Q C + Q AE = Q IS --------------(a)
Q AE = Q IS － Q H － Q R － Q C

## Slide 20: Presumption of Heat Balance
  Q AE = Q IS － Q H － Q R － Q C
QAE : Turbulent Heat Transfer
QH : Expended Heat by Watering
QIS : Heat for Snow-melting
QC : Conductive Heat of Slab
Slab Surface
QR : Quantity of
Radiation Balance

## Slide 21: Specification of Sprinkler System
Amount of water sprinkling | 1.0 liters / min. /m2
Designed water temperature | 10.6 ℃ ～ 11.8 ℃
Method | Circulation of heated water
Water source | Water inflow from tunnel and a river water
Interval between sprinklers | 6 m (staggered layout)

## Slide 22
In case of heavy snowfall
Measures against Snow and Ice
Sprinkling of water
（ Tohoku Shinkansen ）
Snow melting
（ Conventional line ）

## Slide 23: Snow Shelter
Upper left : Over view of snow shelter in conventional line
Lower left : inside view of snow
shelter over the turnouts
Lower right : Front view of snow
shelter over the turnout in station
Snow Shelter over the turnouts at conventional line

## Slide 24: Snow-melting with Sprinkler Spray

## Slide 25: Snow Removal with Heated Water Jet at Tongue Rail of Scissors Crossing

## Slide 26: Kinds of Equipment on Measures against Snowfall
Equipment of Measures Against Snow Damage
Snow Protection Equipment
Snow melting Equipment
Snow Storage Equipment
Snow Shelter
Snow Jet
Snow Melting Equipment with Watering
Open Floor type Viaduct
Snow Melting Equipment with Heated Water
Water Intake Base
Equipment at Snow Melting Base
Far Monitoring Equipment
Heated Water Jet
Floor Slab Heating Type
Pocket type Snow Storage
Semi-snow Shed Type Snow Storage
Snow Storage
Equipment of Measures Against Snow Damage at Turnout

## Slide 27
Snow-melting by
sprinkler spray
Heated water (50～60℃)
Flow Chart of Sprinkler Spray
ｓｐｒａｙ
Cold water
Snow-melting water
Catchment point
To viaduct
Water pump
Rail
Circulating tank
Dust removing tank
Conduit
Settling tank
Water intake tank
Water storage tank
Heat storage tank
Heater
Water intake
station
Snow-melting base
Wind
velocity
Detection
Temperature
・Start / Stop
Water temperature
Data
Control PC
※ Condition for stopping water sprinkling
No snow fall continues for more than 10 min.
and
Returned water temperature is more than 2℃.
※ Condition for starting water sprinkling
Snow fall of more than 0.25cm/h continues for more than 20 min.
or
Snow fall of more than 0.50cm/h continues for more than 10 min.

## Slide 28
Track Structure（Slab Track）
Tunnel
（ Kyushu Shinkansen ）
Bridge
（ Kyushu Shinkansen ）

## Slide 29: Conclusions
Points of view for selecting High Speed Rail structures:
Selection from a viewpoint of LCC including maintenance cost
Reduction of maintenance cost by adopting slab track in the section of cut and embankment.
Application of asset management by adopting concrete structures such as viaduct and tunnel.
Points of view for utilizing characteristics as high-speed rail:
To secure promptness as exclusive line for passengers
No adoption of surface crossing
Point of view on measures against snow damage in winter for securing punctuality of train operation :
Selection of equipment for measures against snow damage (such as snow storing type, sprinkler spray method, snow shelter,open floor type viaduct)

## Slide 30
Thank you for your attention.